## Slide 1: Deep Learning-based Monitoring of the Urban Traffic using MOBATSIM
Institute of Industrial Automation
and Software Engineering
INTERMEDIATE REPORT
Nikita Jhawar
M.Sc. Electrical Engineering

## Slide 2
TIMELINE
DATA Collection with respect to different possibilities
Fault Injection in MOBATSim
Data Evaluation and PreProcessing
Implementation of DL Model
Analysis and Result Comparison

## Slide 3
FAULT INJECTION

## Slide 5
FAULT DETAILS
Vehicle | Target Component | Target Variable | Fault type | Fault duration | Injection Type
Vehicle 2 | Speed Sensor | Speed Reference | Noise, StuckAt, Offset/Bias | 0.6, 1.2, 1.8, 2.4, 3.0, 3.6, 4.2, 5 | Uniform (At 10 secs, At 30 secs)
 | Distance Sensor | Intervehicular Distance | Noise, StuckAt, Offset/Bias | 0.6, 1.2, 1.8, 2.4, 3.0, 3.6, 4.2, 5 | Uniform (At 10 secs, At 30 secs)
Vehicle 6 | Speed Sensor | Speed Reference | Noise, StuckAt, Offset/Bias | 0.6, 1.2, 1.8, 2.4, 3.0, 3.6, 4.2, 5 | Uniform (At 10 secs, At 30 secs)
 | Distance Sensor | Intervehicular Distance | Noise, StuckAt, Offset/Bias | 0.6, 1.2, 1.8, 2.4, 3.0, 3.6, 4.2, 5 | Uniform (At 10 secs, At 30 secs)

## Slide 6
COLLECTION AND EVALUATION OF DATASET
Three driving scenarios have been considered: Urban City Traffic, Platoon Control, and Road Merge Collision
Three Error category has been considered: Bias/Offset, Stuck-at fault, and Noise.
For every scenario, 8 faulty cases will be simulated for each error category (80 faulty cases for each category as there are 10 vehicles)
Error values (for offset error), Injection time, and error duration have been predefined and chosen.
Bias/ Offset and Noise takes value 5.
Fault duration can any value in: [0.6, 1.2,1.8, 2.4, 3.0, 3.6, 4.2, 5]
The data is already resampled to a 0.02-sec sampling rate.
A total of 4000 samples are collected in every dataset.

## Slide 7
URBAN CITY TRAFFIC

## Slide 8
PLATOON CONTROL

## Slide 9
ROAD MERGE COLLISION

## Slide 10: FINAL DATA FORMAT
Time | Speed | Rotation | Position | Translation
Seconds | Float | Float | Float | Float
Minimum No. of Attributes: 4
Initial Data Sample Rate: 0.005 seconds
Final Data Sample Rate: 0.02 seconds
Every Simulation Duration: 80 seconds (4000 entries for each simulation)
Total no. of simulations: 30 (Fault-free) + 240*3 (Faulty) = 750
[Faulty data includes fault-free entries where there is no error injection.]

## Slide 12
TOPICS TO DISCUSS
DATA GENERATION: Willing to include dataset for a non-uniform sample as well
DATA PREPROCESSING AND OUTPUT:
FINAL REQUIREMENTS FOR THE THESIS: Need to know if any other processes should be executed.
SUBMISSION: Probable submission date for Thesis by 30th May, 2022

## Slide 13
THANK YOU FOR YOUR
TIME AND ATTENTION